## Slide 1
John Bistline (EPRI)
Coauthors: Geoff Blanford, Neil Mehrotra, Chris Roney, Catherine Wolfram, and David Young Harvard Electricity Policy Group May 31, 2023
© 2023 Electric Power Research Institute, Inc. All rights reserved.
www.epri.com
Energy System Impacts of the Inflation Reduction Act
Insights from EPRI’s US-REGEN Model

## Slide 2: U.S. Regional Economy, GHG, and Energy (US-REGEN)
EPRI’s In-House Energy-Economic Model
Documentation, articles, and reports available at https://esca.epri.com
Integrated
Hourly Load, Renewables, and Prices
Electric Generation
Energy Use
Detailed representation of:
Energy and capacity requirements
Renewable integration, transmission, storage
State-level policies and constraints
Model Outputs:
Generation, capacity, and end-use mix
Power sector and economy emissions
Detailed representation of:
Customer differences across end-use sectors
End-use technology trade-offs
Electrification and efficiency opportunities

## Slide 3: Rapid Buildout of the Grid in All Scenarios
Additions near historical maximum each year through 2030 with incentives
Source: Bistline, Mehrotra, Wolfram (2023), “Economic Implications of the Climate Provisions of the Inflation Reduction Act” (link)

## Slide 4: Annual Fiscal Costs of IRA Power Sector Credits in Context
Similar to U.S. almond revenues (~$12 B)
Similar to Disney’s content budget in 2022 (~$33 B)
2x Disney’s annual content budget

## Slide 5: Historical and Projected Power Sector CO2 Emissions
IRA reductions align with historical trends
PTC/ITC in place until power sector emissions reach 25% of their 2022 emissions
  Roughly 80% below 2005 levels
  Threshold reached after 2040 in many IRA scenarios
Source: Bistline, Mehrotra, Wolfram (2023), “Economic Implications of the Climate Provisions of the Inflation Reduction Act” (link)

## Slide 6: Policy Design Shapes Power Sector Outcomes
2050 Wholesale Electricity Price Duration Curve in SPP Region
Subsidies could increase frequency of negative wholesale prices, even while retail declines are modest
Source: Bistline, Mehrotra, Wolfram (2023), “Economic Implications of the Climate Provisions of the Inflation Reduction Act” (link)

## Slide 7
EPA released proposed rules in May under Clean Air Act 111(b) and (d)
111(b) and (d)
Analysis examines how design decisions could impact investments, emissions, costs
Design Decisions
Analysis of potential implications of new and existing source performance standards for the U.S. power sector
EPRI White Paper on 111 Performance Standards
April 4
Release of 111 white paper, which is free on epri.com to download (ID #3002026291)

## Slide 8: Illustrative Abatement Costs with 111(d) Options
Marginal abatement costs can be order-of-magnitude higher for H2 cofiring than gas cofiring at coal plants; IRA incentives are largest for coal CCS retrofits and electrolytic H2 production
IRA
Ref
Range reflects gas price $3-6/MMBtu
Range reflects capital costs from $2,800-3,900/kW
Range reflects gas price $3-6/MMBtu
Range reflects H2 cost of $4-5.5/kg (and 45V credits)
Range reflects capital costs from $1,250-1,800/kW

## Slide 9: Power Sector CO2 Emissions: IRA and 111 Standards
PTC/ITC in place until power sector emissions reach 25% of their 2022 emissions
  Roughly 80% below 2005 levels
  Threshold reached after 2040 in many IRA scenarios
Performance standard design decisions—esp. their trading provisions, form, stringency—materially alter outcomes
  Ranges reflect policy design
  CCS standards are considerably more costly than cofiring standards but achieve greater CO2 reductions
Many caveats on deployment timelines, infrastructure, costs
111 Cofiring Standards
111 CCS Standards

## Slide 10: Key Takeaways
IRA, along with other policies and market trends, shift “reference” scenarios away from natural gas and coal generation and toward low-CO2 resources
  Coal declines faster than gas, and gas generation declines faster than gas capacity
  IRA continues to drive emissions reductions beyond 2030: Power sector CO2 could fall ~60% below 2005 by 2030 and ~80% by 2035
111(d) design decisions alter CO2, cost, and generation outcomes
  Flexibility (e.g., across plants and regions), form, and stringency are key
  CCS-based standards are significantly more costly than cofiring-based ones but lead to lower emissions
Modeling IRA impacts is challenging
  Many subjective modeling decisions, given IRA’s complexity and pending guidance
  Range of possible outcomes based on different interpretations
Many uncertainties moving forward about policy, market, and technological drivers will shape power sector trajectories

## Slide 11
Micro/macro economic implications of climate provisions of IRA (link)
Brookings IRA Analysis
Analysis of implications of new and existing source performance standards for the U.S. power sector (link)
111 Design Decisions
For More Information
Reports referenced in today’s presentation
Impacts of IRA, 50x30 policies, and inflationary drivers (link)
Near-Term Decarbonization Drivers

## Slide 13: Bibliography
Bistline, Mehrotra, Wolfram (2023), Economic Implications of the Climate Provisions of the Inflation Reduction Act, Brookings Papers on Economic Activity
Bistline, et al. (2022), Actions for Reducing U.S. Emissions at Least 50% by 2030, Science
Bistline, et al. (2022), Economy-Wide Evaluation of CO2 and Air Quality Impacts of Electrification in the United States, Nature Communications
Bistline (2021), Roadmaps to Net-Zero Emissions Systems: Emerging Insights and Modeling Challenges, Joule
Bistline, et al. (2021), Deep Decarbonization Impacts on Electric Load Shapes and Peak Demand, Environmental Research Letters
Bistline, et al. (2021), Canadian National Electrification Assessment: Electrification Opportunities for Canada’s Energy Future, EPRI Report 3002021160
Blanford, et al. (2023), Net-Zero 2050: U.S. Economy-Wide Deep Decarbonization Scenario Analysis, EPRI Report 3002024882
Browning, et al. (2023), Net-Zero CO2 by 2050 Scenarios for the United States in the Energy Modeling Forum 37 Study, Energy and Climate Change
For more information, see our website at https://esca.epri.com

## Slide 14: U.S. Greenhouse Gas Emissions and Future Targets
Historical emissions from U.S. EPA’s “Inventory of U.S. Greenhouse Gas Emissions and Sinks”
Electric
Industry
Buildings
Transport
Non-Energy CO2
Non-CO2 GHGs
2005
2021
2030 (U.S. NDC)
How would net-zero emissions be reached?
Energy CO2 Emission Changes 2005–2021
  Electric 35%
  Industry 9%
  Transport 8%
  Buildings 5%
2050 Net Zero

## Slide 15: Inflation Reduction Act (IRA) Modeled Provisions
Provisions shown next to applicable section
Electricity
13101: Production tax credit (PTC) extension
13102: Investment tax credit (ITC) extension
13103/13702: Solar in low-income communities
13015: Production tax credit for existing nuclear
13701/13702: New clean electricity PTC (45Y) and clean electricity ITC (48E)
Multi-Sector
13104: Extension of credits for captured CO2 (45Q)
13204: Production credits for clean hydrogen (45V)
Transport
13401: Clean vehicle credit
13403: Commercial clean vehicle credit
13404: Alternative refueling property credit
Buildings
13302: Residential clean energy credit
13303: Energy efficient commercial building deduction
13304: Energy efficient home credit
50121: Home energy efficiency credit
50122: High efficiency home rebate program
Select Provisions Not Modeled
13201/13202: Extension of incentives for biofuels*
13203: Sustainable aviation credit*
13402: Credit for previously owned clean vehicles
13501: Extension of advanced energy project credit (48C)
45Q/45V limited outside of the power sector*
50161: Industrial facilities deployment program
Agricultural conservation and forestry
*Provisions we will be able to represent in LCRI model
Omission of provisions from modeling has ambiguous effects on emissions outcomes

## Slide 16
Up to ~$30/MWh (for 10 years), with complex bonus rules
Replaces existing credits for wind/solar starting in 2025 for all technologies with “emissions intensity not greater than zero”
IRA §13701
Clean Electricity Production Credit
30% with labor bonus with 10 p.p. bonuses for domestic content and energy communities
Standalone storage is eligible (in addition to PTC-eligible technologies)
Like PTC, extends until power CO2 is 25% of 2022 levels (or 2032)
IRA §13702
Clean Electricity Investment Credit
Up to $85/tCO2 captured with bonus
12-year eligibility
Must begin construction by 2032
Projects cannot stack 45Q and other credits
Like 45V, no bonuses for domestic content/EC
IRA §13104
CO2 Capture & Storage Credit
Depends on lifecycle GHG intensity of production, measured by ANL’s GREET model
Up to $3/kg with 10-year eligibility (must begin construction by 2032)
Can be “stacked” with 45Y or 48E for electrolytic hydrogen
IRA §13204
Clean H2 Production Credit
45Y
48E
45Q
45V
Key Electric Sector IRA Provisions
Major Tax Credits with Electric Sector Implications
NB: All dollar figures here refer to 2022 dollars; bill includes adjustments for inflation in future years

## Slide 17: Cost Estimates for Generation/Storage Technologies
Solar PV
Onshore Wind
Battery (4-Hour)
NGCC
Higher Costs Scenario
Lower Costs Scenario
2022 estimates based on EPRI report 3002024231 (link)
Sensitivities examine uncertainty about the persistence of near-term cost escalations
Present (2022)
Present (2022)
Present (2022)
Present (2022)

## Slide 18: Natural Gas Price Scenarios
Higher vs. Lower Costs (i.e., slow vs. fast recovery) scenarios span $2/MMBtu range by 2030
Prices in real 2022 U.S. dollar terms

## Slide 19: IRA Lowers Economy-Wide Emissions
IRA, combined with existing policies and technology trends, lowers CO2 emissions, esp. from electricity and transport
  Range of reductions possible depending on implementation, additional policies, and macro context (interest rates, costs, etc.)
  Most of 2030 reductions under IRA come from power sector (70-74%)
Power sector leads additional reductions for 50x30 targets, similar to projections from the Science article on these targets
IRA helps to lower 2030 emissions, but additional reductions are needed from all sectors to meet 2030 targets; electricity plays a key role in direct and indirect reductions through electrification

## Slide 20: Retail Electricity Prices
Source: Bistline, Mehrotra, Wolfram (2023), “Economic Implications of the Climate Provisions of the Inflation Reduction Act” (link)

## Slide 21: Electricity Generation

## Slide 22: IRA’s Fiscal Costs and Abatement Costs
Fiscal costs through 2031 span wide range ($400-1,200 B)
  0.9 to 4x initial estimates due to higher clean energy deployment
  10-year fiscal costs align with Credit Suisse and Goldman Sachs ($800-1,200 B)
Average abatement costs range from $36-87/t-CO2
  Discounted total resource costs divided by CO2 reductions
  Reflects uncertain technologies, markets, and policies
Although fiscal costs are higher than initial estimates, average abatement costs are likely below social cost of CO2 estimates, even before accounting for air quality co-benefits
Avg. abatement Cost ($/t-CO2)
$61-87/t-CO2
$45-61/t-CO2
$36-49/t-CO2

## Slide 23: Policy Design Shapes Power Sector Outcomes
Comparing U.S. Inflation Reduction Act (IRA) subsidies vs. equivalent carbon tax
  Taxes have lower coal generation and lower abatement costs
  Subsidies have lower el. prices
IRA’s fiscal costs to 2032 span wide range ($400-1,200 B)
  0.9 to 4x initial estimates due to higher clean energy deployment
  Carbon tax would raise revenue
Policy design has first-order implications for resource investments, operations, cost, and emissions
Source: Bistline, Mehrotra, Wolfram (2023), “Economic Implications of the Climate Provisions of the Inflation Reduction Act” (link)

## Slide 24: Appropriate Metrics for Measuring CO2 Reductions?
Source: Bistline, et al. (2022), “Economy-Wide Evaluation of CO2 and Air Quality Impacts of Electrification in the United States” (link)
Short-run marginal emissions approaches can underestimate CO2 reductions from electrification by 32-91%

## Slide 25: EPRI Publications on Reaching the 2030 U.S. Climate Target
Systems Modeling
Impacts of Inflationary Drivers and Updated Policies on U.S. Decarbonization (3002026229)
Free EPRI report available published in Mar. 2023
US-REGEN analysis 2030 targets and Inflation Reduction Act impacts
Wide range of “what-if” scenarios
Actions for Reducing U.S. Emissions at Least 50% by 2030
Published in Science in May 2022 (author link)
Multi-model comparison with authors and models from EDF (EDF-NEMS), EPRI (US-REGEN), LBNL (ReEDS + PLEXOS + FACT), MIT (USREP-ReEDS), PNNL (GCAM-USA-AP), NRDC (EnergyPATHWAYS + RIO)
Strategies and Actions for Achieving a 50% Reduction in U.S. Greenhouse Gas Emissions by 2030 (3002023165)
Free EPRI report available published in Nov. 2021
US-REGEN analysis of electric sector and economy-wide wide reductions
Issue Deep Dives
Enhancing Energy System Reliability and Resiliency in a Net-Zero Economy (3002023437)
Leveraging Existing Infrastructure: Increasing the Capacity of Transmission Lines (3002023004)
Technology Innovation: A Roadmap to Leverage Existing Nuclear Power Plants to Increase Zero-Carbon Energy Production (3002022700)
Electric Utility Workforce Development and Decarbonization (3002023229)
Maximizing Distributed Energy Resource Value Through Grid Modernization (3002023235)
Supply Chain Risks and Needs to Support Electric Utility Sector Decarbonization (3002023228)